## Slide 1
  Jaka Pribošek, Matija Brumat
University of Ljubljana
Faculty of Mechanical Engineering
  Supervised by prof.dr. Janez Diaci
jaka.pribosek@fs.uni-lj.si
matija.brumat@fs.uni-lj.si

## Slide 2
Why a deformable mirror ?
Adaptive imaging

## Slide 3
Why a deformable mirror ?
Adaptive imaging
Aberration compensation
Source: NASA

## Slide 4
Why a deformable mirror ?
Precision light manipulation
Adaptive imaging
Aberration compensation
Source: NASA
Source: Elliot Scientific
Source: TU WIen
Technology, limited to priviliged institutions- what about others?

## Slide 5
How does it work?
Piezoelectric diaphragm
Segmented electrodes
Curvature proportional to applied voltages
3 DoF : tip, tilt, defocus

## Slide 6
The fabrication
Piezo buzzer
Coat with paint
Mark the electrodes
Etch the mounting arms
Solder wires
Glue the mirror

## Slide 7
The electronics
10 TI integrated circuits
The heart is a quad bipolar DAC, amplified up to ±50 V
Ultra low-noise and high voltage switching power supplies
Microprocessor unit with onboard trajectory processing

## Slide 8
The complete system

## Slide 9
Results
Processing speed: 75000 points/s
Angular deflection range: ±0.63°
Sensitivity: 0.02 mrad/V
Step response: 5 µs rise time, 6 % overshoot

## Slide 10
Results
Processing speed: 75000 points/s
Angular deflection range: ±0.63°
Sensitivity: 0.02 mrad/V
Step response: 5 µs rise time, 6 % overshoot

## Slide 11
Results
Processing speed: 75000 points/s
Angular deflection range: ±0.63°
Sensitivity: 0.02 mrad/V
Step response: 5 µs rise time, 6 % overshoot

## Slide 12
Summary
In 6 months we have developed:
  a low-cost mirror fabrication
  required electronics
  optical system
  software
  Final system…
TI Eval Boards for feasibility study
Webench for optimal analog design
Layout recomendations
TI free samples
Code examples (MSP430ware)
Top-down development approach
  …that anyone can build at home !

## Slide 13
…and our future plans ?
Future is TI.
….almost accomplished in the meantime!
  confocal microscopy
  3D topography inspection
  analog peak detection circuitry
…5 more TI devices here…