## Slide 1
A Wearable Embedded System for Wireless Acquisition of Vital Parameters
Laboratory of Medical Electronics (LME)
Lübeck University of Applied Sciences
Roman Kusche, Paula Klimach, Ankit Malhotra, and Martin Ryschka

## Slide 2: Motivation
https://pixabay.com/en/world-map-earth-global-continents-146505/
http://www.who.int/cardiovascular_diseases/publications/atlas_cvd/en/
http://newsroom.heart.org/news/new-statistical-update-looks-at-worldwide-heart-stroke-health
  An estimated 17.5 million people died from CVDs in 2012, representing 31% of all global deaths.
  CVDs are the leading cause of death in the world

## Slide 3: Motivation
State-of-the-art portable commercial patient monitoring devices measure Electrocardiogram (ECG), Photoplethysmogram (PPG), physical motions of the patient…
In addition to measurements currently available, our device provides an improved method for measuring “Pulse Wave Velocity.”
Gary F. Mitchell et al.: Arterial Stiffness and Cardiovascular Events, Circulation, 121, 2010, 505-511

## Slide 4: Measurement of the Pulse Wave Velocity (PWV)
Δx
t2: Pulse Wave Arrival
Pressure changes in the sealed ear canal
t1: Pulse Wave Start
Heart Sounds
(1)
http://wikipedia.es

## Slide 5: InEar-Sensor
Sensor
Pressure Changes (t2) &
Heart Sounds (t1)
Just ONE sensor to acquire 2 signals (Pressure + Heart Sounds)
Simple principle
Easy to use
Cheap (<1 €/Sensor)
http://de.wikipedia.org

## Slide 6: Measurement System
Mic. Amp.
Patient
InEar Sensor
ADC
µC
USB
Mic. Amp.
Mic. Amp.
Mic. Amp.
ECG
PPG
Acc. Sens.
Bluetooth
µSD Card
Power Supply (Li-Ion)
PC
Smartphone
Can you prove that you are measuring heart sounds?
An ECG to compare the signal timing would be helpful!
An additional technique to prove the arrival of the PW would be good!
Physical motions of the patient could be interesting in the future!
The device should be portable!
ADC
ADC
ADC
Keep it simple, compact and cheap!
LMV844MT
LMV844MT
LMV844MT
LMV844MT
ADS131E06
LMX9838
TPS63001, TPS73025, TPS72325
ADS131E06
ADS131E06
INA126E, LMV844
OPA380
http://freestockphotos.biz
http://pixabay.com
http://de.wikipedia.org

## Slide 7: The Right ADC to Save Components
Typical problem:
Typical Solution: Filtering
  DC and AC are important
  DC/AC ≈ 1000
Our Solution:
  High resolution ADC (ADS131E06)
  ENOB(1kSPS) = 20.4 Bits
  Ideal Case: ≈ 10.4 Bits left for AC component
http://www.ti.com/graphics/folders/partimages/ADS131E06.jpg

## Slide 8: Realization

## Slide 9: Results (RAW Data)

## Slide 10: Conclusion
Less components because of usage of high resolution ADC (ADS131E06)
Analog circuits were simplified but still deliver high quality data
The system has portability and is low-cost
Wearable system for acquisition of:
ECG
PPG
Heart Rate Variability
Acceleration
Conventional (Cardiovascular)
Parameters
Pulse Wave Velocity
Cardiovascular
Prognostic Marker

## Slide 11: Thank you for your attention
Grant number 13EZ1140A/B
http://lme.fh-luebeck.de
Roman Kusche1,2, Paula Klimach1,2, Ankit Malhotra1,2,3, and Martin Ryschka1
1Laboratory of Medical Electronics, Lübeck University of Applied Sciences, Lübeck, Germany
2Graduate School for Computing in Medicine and Life Sciences, Universität zu Lübeck, Lübeck, Germany
3Institute of Medical Engineering, Universität zu Lübeck, Lübeck, Germany